## Slide 1
Fitting and Machining
N2

## Slide 2
www.futuremanagers.com
INTRODUCTION
Regulations are applicable to all students associated with the metal industry. Occupational safety is of cardinal importance in any workshop situation. Safety must be priority number one at all times. When an accident does happen, everyone loses, the worker with pain and suffering, the company loses production and has unwanted down time.
Module 1: Occupational Health and Safety (Act No. 85 of 1993)

## Slide 3
www.futuremanagers.com
Module 1: Occupational Health and Safety (Act No. 85 of 1993) (continued)
DANGEROUS PLACES
A dangerous place is, for example, is a pit over which trucks and similar vehicles park so that you can work underneath more easily. This is a dangerous place when there is no vehicle over the pit. The pit should have a safety railing around it when it is not in use to prevent people falling in and being injured.

## Slide 4
www.futuremanagers.com
Module 1: Occupational Health and Safety (Act No. 85 of 1993) (continued)
REGULATIONS APPLICATION TO THE MINERALS ACT
Rules include but are not limited to:
Waste paper must not be stored in quantity where it can be a fire hazard.
Large quantities of paper or other flammable material should not be stored near electrical equipment.
Workers working or travelling in an unlit part of a mine must have suitable lights with them.
Only lamps that are approved are allowed in fiery mines.

## Slide 5
www.futuremanagers.com
Module 1: Occupational Health and Safety (Act No. 85 of 1993) (continued)
LOSE OUTER CLOTHING
No loose outer clothing may be worn in close proximity to machinery. Loose fitting clothing that flaps about, has loose sleeves, attached untied belts or attachments could be caught even when passing close by stationary objects, let alone moving machines or rotating shafts is extremely dangerous.

## Slide 6
www.futuremanagers.com
Module 1: Occupational Health and Safety (Act No. 85 of 1993) (continued)
GENERAL MACHINERY PROTECTION
Includes but is not limited to:
The working area around all machines must be clearly marked.
All moving parts on all machines must be covered by guards.
No machine may be operated if any of the guards is missing or broken.
No hand tools may be left on machinery, especially when operating.
Never lean on machinery.

## Slide 7
www.futuremanagers.com
INTRODUCTION
The main function of couplings is to join two shafts together or to provide a mode of conveying or transmitting power from a drive source to a machine. A coupling can, for example, connect a steam turbine to an alternator or an electric motor to a pump. By means of a coupling machine, components, are tightly coupled and cannot be easily disengaged.
Module 2: Couplings

## Slide 8
www.futuremanagers.com
Module 2: Couplings (continued)
THE DIFFERENCE IN APPLICATION BETWEEN A COUPLING AND A CLUTCH
A coupling is a device that positively connects two (input and output) shafts to transfer rotation from one to the other.
A clutch is a device by which two shafts or rotating members may be connected or disconnected, either while at rest or when in relative motion.

## Slide 9
www.futuremanagers.com
Module 2: Couplings (continued)
CLASSIFICATION OF COUPLINGS
Couplings can be categorised into three groups:
Permanent couplings.
Self-aligning couplings.
Flexible couplings.

## Slide 10
www.futuremanagers.com
Module 2: Couplings (continued)
DIFFERENT KINDS OF COUPLINGS
Permanent (fixed) coupling | Self-aligning coupling | Flexible coupling
Flange | Hooke/universal | Raffard
Marine | Constant Velocity (CV joint) | Nylon sleeve
Chain | Metal disc/Oldham | Pin and rubber bush
Gear |  | Spider
Fluid drive |  | Rubber belt/tyre/elastomeric
Muff |  | Resilient/bibby/steel grid

## Slide 11
www.futuremanagers.com
HISTORY OF THE SYSTÊME INTERNATIONALE (SI) OF UNITS
The creation of a decimal metric system during the French Revolution and the subsequent use of two platinum rods representing the meter (and now stored in vaults in Paris and New York), was the first step in the development of the present SI system. In 1832, Gauss promoted the metric system as a system of units for physical science.
Module 3: Limits and fits

## Slide 12
www.futuremanagers.com
Module 3: Limits and fits (continued)
SYSTEMS OF MEASUREMENT
No loose outer clothing may be worn in close proximity to machinery. Loose fitting clothing that flaps about, has loose sleeves, attached untied belts or attachments could be caught even when passing close by stationary objects, let alone moving machines or rotating shafts is extremely dangerous.

## Slide 13
www.futuremanagers.com
Module 3: Limits and fits (continued)
INTERCHANGEABILITY OF PARTS
Most measurement in the modern world conforms to either the English (British Imperial) system or the metric (International System of Units). The metric system is now chiefly used by most industrialised nations of the world.

## Slide 14
www.futuremanagers.com
Module 3: Limits and fits (continued)
TYPES OF FIT
Fits may be classified into three types:
Clearance fit;
Interference fit; or
Transition fit.

## Slide 15
www.futuremanagers.com
INTRODUCTION
A bearing is the link between the stationary housing and the rotating, reciprocating or sliding part. The bearing provides maximum support with minimum resistance to motion.
Module 4: Bearings

## Slide 16
www.futuremanagers.com
Module 4: Bearings (continued)
TYPES OF BEARINGS
Different types of bearings include:
Solid bearings;
Split bearings;
Part bearings;
Bushes;
Pedestal bearings;
Plumber block bearings;
Taper bearings; and
Hanger bearings.

## Slide 17
www.futuremanagers.com
Module 4: Bearings (continued)
MAINTENANCE OF BEARINGS
The maintenance of plain bearings is needed to prevent failure.

## Slide 18
www.futuremanagers.com
Module 4: Bearings (continued)
CATEGORIES OF PLAIN BEARINGS
Plain bearings are categorised according to the loads they have to carry:
Radial loads are carried by pedestal, plumber block, plain split, hanger and footstep bearings.
Axial loads are carried by thrust bearings such as single- and multi-collar, Michel, thrust washers and a variety of taper bearings.
Combined load carrying bearings include pedestal bearings, plain split bearings, footstep bearings, and taper-lock bearings.

## Slide 19
www.futuremanagers.com
Module 4: Bearings (continued)
MATERIALS
The most commonly used materials in plain bearings are:
Cast-iron;
Bronze;
White-metal;
Nylon; and
Teflon.

## Slide 20
www.futuremanagers.com
Module 4: Bearings (continued)
ADVANTAGES OF PLAIN BEARINGS
The initial cost is low as they are of simple construction.
They run quietly as there is no metal to metal contact.
Plain bearings are simple to fit or replace especially in crankshafts and to other awkward places, as they are not press or heat fitted.
They absorb shock better than roller bearings due to the cushion of oil.
They do not suffer from metal fatigue as there are no moving parts.

## Slide 21
www.futuremanagers.com
Module 4: Bearings (continued)
DISADVANTAGES OF PLAIN BEARINGS
There is higher initial drag when starting up than with roller bearings.
They are reliant on a constant pressure supply of clean oil.
Should there be a break in pressure or supply, damage will occur.
Some power is lost in overcoming friction.
Damage is incurred if the oil transmits foreign particles or has a viscosity which is too low.

## Slide 22
www.futuremanagers.com
Module 4: Bearings (continued)
RUBBER AND METAL SEALS
Both rubber, metal and a combination of both types of seals are used in conjunction with bearings. The bearing allows movement and supports the shaft while the seal prevents oil or other liquids from leaking and dirt getting in.

## Slide 23
www.futuremanagers.com
Module 4: Bearings (continued)
COMPONENTS OF ANTI-FRICTION BEARINGS
Anti-friction bearings, are made up of the components shown below:

## Slide 24
www.futuremanagers.com
Module 4: Bearings (continued)
OPERATION, MAINTENANCE AND USES OF ANTI-FRICTION BEARINGS
In gearboxes and differentials, anti-friction bearings are semi-submerged in oil or splash fed and the lubricant merely flows over them, cooling and cleaning them at the same time. This type of bearing can operate at both
high and low revolutions with varying loads. The only maintenance they require is regular inspection and sufficient, clean lubricant of good viscosity.

## Slide 25
www.futuremanagers.com
Module 4: Bearings (continued)
DIFFERENT BEARINGS FOR DIFFERENT LOADS
Radial loads are the type of loads experienced by big-end and journal bearings in a petrol or diesel engine, the load is at 90º to the shaft.
An angular load is a compound load that is partially radial and partially thrust, requiring either a bearing especially designed to handle the combined loads or a combination of a radial bearing and a thrust bearing.

## Slide 26
www.futuremanagers.com
Module 4: Bearings (continued)
ADVANTAGES OF ANTI-FRICTION BEARINGS
The bearings can be pre-packed with grease, sealed and mounted outside.
They do not just suddenly break down, they make warning noises which become louder as the state of the bearing gets worse.
They are more suitable in gear boxes as they have less starting resistance and do not have to build up oil pressure before they become fully efficient.
They can run under overloads and without lubrication for short periods.

## Slide 27
www.futuremanagers.com
Module 4: Bearings (continued)
DISADVANTAGES OF ANTI-FRICTION BEARINGS
They cannot be fitted to average, normal, one piece crank-shafts or cam-shafts.
They are noisier than plain bearings especially at constant high speeds like in motor car engines.
Unlike plain bearings, they should be replaced when they no longer work.
The initial cost outlay is usually much higher.

## Slide 28
www.futuremanagers.com
INTRODUCTION
One of the best ways of reducing friction from moving parts (which causes wear and build-up of heat) is to use a suitable lubricant. Lubrication reduces friction to a minimum by the replacement of solid friction with fluid friction.
Module 5: Lubrication

## Slide 29
www.futuremanagers.com
Module 5: Lubrication (continued)
TYPES OF LUBRICANTS
Lubricants are generally classified into three groups:
Solid;
Semi-solid (also grease); or
Liquids.

## Slide 30
www.futuremanagers.com
Module 5: Lubrication (continued)
HYDRODYANAMIC LUBRICATION
Hydrodynamic lubrication takes place when two surfaces (bearing and shaft) are not physically touching each other but a thin film of oil is sandwiched between the two moving contacts (surfaces). The only resistance is the resistance of the oil itself. This state is called hydrodynamic lubrication.

## Slide 31
www.futuremanagers.com
Module 5: Lubrication (continued)
PROPERTIES A LUBRICANT MUST DISPLAY
Maintain relatively stable body over a wide load and temperature range.
Must prevent formation of sludge, gum and varnish.
Maintain its own stability and therefore reduce replacement costs.
Should not react with the lubricating surface and should have no acidity.
Depress foaming or have non-foaming characteristics.
Must have a high flash point (non-flammable).
Non-toxic, with good unifying and adhesive characteristics.

## Slide 32
www.futuremanagers.com
Module 5: Lubrication (continued)
LUBRICATING DEVICES
The purpose of a lubricating device is to supply oil or grease to different machine components in a precise manner. Lubricating devices include:
Oil gun;
Oil can;
Oil cup;
Grease gun;
Needle (bottle) lubricator.

## Slide 33
www.futuremanagers.com
Module 5: Lubrication (continued)
CUTTING FLUIDS AND CUTTING OILS
Cutting fluids and cutting oils are important for extending the life of a cutting tool and improving cutting action. Cutting oils are generally divided into what are termed “fixed” oils and mineral oils. The “fixed” oils may consist of animal. Mineral oil comes from crude oil and paraffin is an example of this class.

## Slide 34
www.futuremanagers.com
THE FUNCTION OF A VALVE
A valve is a device that is used to seal off an inlet or outlet point when required, and to allow flow, with minimum resistance when flow is required. Valves must be able to control the rate of flow, the pressure and the direction of flow.
Module 6: Valves

## Slide 35
www.futuremanagers.com
Module 6: Valves (continued)
BASIC WORKING PRINCIPLES OF A VALVE
A valve must be as simple as possible to operate and maintain while being highly efficient, durable and long lasting.

## Slide 36
www.futuremanagers.com
Module 6: Valves (continued)
TYPES OF VALVES
Gate valves;
Diaphragm type valves;
Safety valves (for gas and steam pipe lines);
Relief valves for liquids;
Non-return valves;
Butterfly valves;
Ball valves; and
Foot valves.

## Slide 37
www.futuremanagers.com
THE BASIC FUNCTIONS OF PACKING AND SEALS
The main reason for using packing and seals is to prevent gasses or liquids from leaking at critical points in a transfer system. A second function of seals and packing is to prevent dust or other impurities from entering a system where it could contaminate the gas, liquid or what ever the system is carrying. Damage could also be done to bearings, slides, joints etc. should any unwanted substances enter the system.
Module 7: Packing, stuffing boxes and joints

## Slide 38
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
TYPES OF PACKING MATERIALS AND SEALS USED ON SYSTEMS CONTAINING WATER, AIR OR STEAM
Rubber;
Neoprene;
Nylon;
Telfon;
Aluminium; and
White metal.

## Slide 39
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
O-RINGS
When fitting O-rings or other seals make sure that the area where the seal is to be fitted is clean and smooth with no sharp edges or threads that could damage the seal. When there are slots, groves or threads over which the seal has to pass they must be covered with plastic tape or other similar material to ensure that the seal is not damaged. Make use of a suitable lubricant like copper-slip on the seal before sliding it into position.

## Slide 40
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
PACKING A STUFFING BOX
When packing a stuffing box make sure that the packing material used is the right thickness and length. The material and coating must be suitable for the type of gas, steam or liquid to be moved.

## Slide 41
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
JOINTS AND BENDS COMMONLY USED IN INDUSTRY
Flanges;
Expansion joints;
Continuous expansion bends;
Packed expansion sliding joint; and
Corrugated expansion joint.

## Slide 42
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
USING JOINTING MATERIAL
Jointing material is used to improve the sealing capacity of the joint, for example, a gasket made of a material suitable for the conditions required. The material must be able to be compressed at one end more than the other to take up slight misalignment or imperfections on the machined faces of the flanges.

## Slide 43
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
THE FAILURE OF FLANGED JOINTS
Joint could fail because:
The packing material used was not suitable for the conditions.
The joint was not tightened evenly or not sufficiently tight.
The flanges were too far out of alignment.
The joint could have been damaged or become loose due to vibration.
The joint could have become corroded, or the packing could have cracked.

## Slide 44
www.futuremanagers.com
Module 7: Packing, stuffing boxes and joints (continued)
THE LAGGING (INSULATION) OF WATER AND STEAM PIPE LINES
Steam pipes are lagged to prevent them from losing heat.
Water pipes are lagged to prevent the water in them from getting too cold or from freezing.

## Slide 45
www.futuremanagers.com
PIPE SIZES AND TERMS
If you measured the pipe diameter on the outside, just to the right of the thread, you would get the outside diameter. Half the difference between the outside diameter and the inside diameter is the pipe thickness.
Module 8: Water pipe systems (up to 50mm diameter)

## Slide 46
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
JOINING METHODS OF STEEL WATER PIPES
Bell-and-spigot method: This method is not common in an average water pipe system. Welded joint: Pipes can be effectively joined by welding both pipe ends together. Soldered or brazed: This method of joining two pipes is usually done by using a collar into which both pipe ends are fed, from opposite ends. Screwed (threaded) joint: The most common method of joining steel pipes is by screwing them together. Flanged joint: Larger pipe lines make regular use of flanged joints.

## Slide 47
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
PLASTIC WATER PIPES
Different types of joints include:
Butt-and-strap joint;
Welded plastic pipe joint;
Screwed (threaded) plastic pipe joints;
Flanged plastic pipe joints.

## Slide 48
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
THERMOPLASTIC PIPING
This type of plastic becomes pliable when heated and can then be worked into desired shapes and angles. The process can be repeated over and over again. It is used for piping, ducts etc. It can also be used as an insulator around a conductor. Polyethylene (PE), in contrast, is not suitable for piping but is used for sheeting.

## Slide 49
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
THE ADVANTAGES OF PLASTIC PIPING
Plastic pipes are corrosion resistant and resistant to most acids as well.
Plastic pipes are extruded and have a smooth finish which requires no further work or finishing such as paint.
Plastic pipes are lighter than steel ones and are therefore easier to handle.

## Slide 50
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
THE DISADVANTAGES OF PLASTIC PIPING
Plastic pipes cannot handle high pressure and heat, like super-heated steam.
The sun’s rays make plastic pipes brittle after extended exposure.
Plastic piping would not be able to handle the high pressure needed for hydraulics.

## Slide 51
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
PIPE CUTTERS AND REAMERS
Pipe cutters rather than a saw are used to obtain a length as the cut is neater and needs no touching up afterwards.
Pipe reamers are used to remove burrs and edges left during the cutting process.

## Slide 52
www.futuremanagers.com
Module 8: Water pipe systems (up to 50mm diameter) (continued)
MATERIALS USED TO SEAL THREADED PIPE JOINTS
The old fashioned method of using sisal string wound into the threads of steel pipes still works, it is just not as quick and easy as using PVC tape.
Using a liquid copper jointing compound is another option.
Teflon is another option for pipe joints.

## Slide 53
www.futuremanagers.com
INTRODUCTION
Pumps are the most extensively used machines in various sectors of industry. Almost all processes are dependent on transporting liquids or transferring energy through liquids. The suction head is the vertical distance measured given (expressed) in meters, from the centreline of the pump to the free level of the liquid to be pumped.
Module 9: Pumps

## Slide 54
www.futuremanagers.com
Module 9: Pumps (continued)
FUNCTION OF A PUMP
A pump is a mechanical displacement device. It is called a displacement device because it displaces fluid or liquids from one location to another.

## Slide 55
www.futuremanagers.com
Module 9: Pumps (continued)
CENTRIFUGAL PUMPS
This pump is classified as a non-positive displacement pump. The centrifugal pump operates by means of centrifugal force. It consists of an impeller, an inlet (eye) and outlet. The impeller consists of vanes which force the fluid or liquid to the periphery (involute casing) as it is sucked through the inlet. This motion creates a centrifugal force.

## Slide 56
www.futuremanagers.com
Module 9: Pumps (continued)
ROTARY PUMPS
The prime mover of a hydraulic system, analogous to the electric motor or internal combustion engine, is the hydraulic pump. There are many types of pumps with a wide range of flow capacities. The four basic designs are
The gear;
Vane;
Rotor; and
Piston pumps.

## Slide 57
www.futuremanagers.com
Module 9: Pumps (continued)
STEAM- AND AIR DRIVEN RECIPROCATING PUMPS
There are many applications where pressure operated pumps are preferred to conventional centrifugal and positive displacement pumps. They operate by using steam, compressed air or gas for lifting any type of non-corrosive fluid. High temperature fluids e.g. condensate or oil can be transferred to a higher height or pressure.

## Slide 58
www.futuremanagers.com
Module 9: Pumps (continued)
WATER HAMMER
Water hammer in plunger or piston pumps is caused by a sudden change in the speed at which fluid is moving, together with a proportional change in pressure. This causes a loud hammering in the pipeline, which is called the “knock” sound. Water hammer is a force which can cause damage to pipelines and pump fittings.

## Slide 59
www.futuremanagers.com
Module 9: Pumps (continued)
POSITIVE AND NON-POSITIVE DISPLACEMENT PUMPS
Positive displacement pumps of the rotary and reciprocating kind can be defined as machines which achieve the direct transfer of liquids by mechanical means, not using centrifugal force.
The non-positive displacement pump delivers liquid at a constant flowrate.

## Slide 60
www.futuremanagers.com
THE FUNCTIONS OF COMPRESSORS
The main function of any compressor is to place large volumes of air under pressure and then store it and the energy in the air in a container called a receiver or reservoir. The compressor consists of one or more cylinders into which air is sucked by a retreating piston. At the end of the inlet stroke the piston moves upwards reducing the volume in the cylinder but with the discharge valve opening, the compressed air is forced into the receiver.
Module 10: Compressors

## Slide 61
www.futuremanagers.com
Module 10: Compressors (continued)
RECIPROCATING COMPRESSORS
The compressor shown below is a two-stage reciprocating type with an inlet and a discharge valve in each cylinder:

## Slide 62
www.futuremanagers.com
Module 10: Compressors (continued)
AIR FILTERS AND OTHER COMPONENTS
To compress air successfully, the air entering the compressor has to be clean and free of dust particles or any foreign objects. This is where the air filter comes in. Air filters come in a variety of shapes and sizes.

## Slide 63
www.futuremanagers.com
Module 10: Compressors (continued)
THE MAIN GROUPS OF COMPRESSORS IN USE TODAY
There are five main groups of compressors used extensively in industry today.
Reciprocating compressors;
Vane compressors;
Rotary screw compressors;
Lobe compressors; and
Centrifugal compressors.

## Slide 64
www.futuremanagers.com
SAFETY PRECAUTIONS TO BE TAKEN WHEN WORKING ON OR NEAR V-BELTS
Never work on or near moving V-belts.
Make sure all portions of any belt are totally enclosed by sturdy guards. Never adjust a V-belt while it is in operation under any conditions.
Make sure you select the right belt for the job required, section and length.
Where necessary, make use of a tensioning pulley to achieve the maximum contact angle.
Module 11: V-belt drives

## Slide 65
www.futuremanagers.com
Module 11: V-belt drives (continued)
THE APPLICATIONS OF V-BELTS
V-belts are used extensively to connect shafts that must be driven to those, but are too far apart to use gears. Torque and power are easily transferred from the driving pulley to the driven one, without changing the direction of rotation by connecting them with a V-belt.

## Slide 66
www.futuremanagers.com
Module 11: V-belt drives (continued)
ADVANTAGES OF V-BELTS
V-belts run quietly for a long time without any maintenance needed as is the case with motor car belt drives used from the crankshaft pulley to the alternator, fan, power steering and air-con.
Gears only work when two shafts are right next to each other and chain drives need regular maintenance and lubrication.

## Slide 67
www.futuremanagers.com
Module 11: V-belt drives (continued)
IDENTIFY AND EXPLAIN BELT DRIVE TERMS
The driver pulley: this pulley is the one on the motor.
The driven pulley: this pulley is the one to which the torque is transferred, via the V-belt.
The idler pulley: this pulley is often smaller in diameter than the other two but has no influence on the ratio between the driver and driven pulleys.
Pulley pitch diameter: This is the effective diameter of the pulley that includes one thickness of the belt.

## Slide 68
www.futuremanagers.com
Module 11: V-belt drives (continued)
BELT DRIVE TERM
The average V-belt used today is single, has an included angle of 40° and is available in a variety of standard lengths and in sections between A and E. A is the narrowest belt and E the widest.

## Slide 69
www.futuremanagers.com
Module 11: V-belt drives (continued)
V-BELT SECTIONS
A modern V-belt is made up of a number of sections such as the outer layer which is usually a synthetic rubber compound that is hard wearing and has a high coefficient of friction so that slipping on the pulley is limited.

## Slide 70
www.futuremanagers.com
Module 11: V-belt drives (continued)
THE DIFFERENCE BETWEEN A SINGLE- AND A MULTIPLE-BELT DRIVE
The difference between a single and a multiple-belt drive is shown in the two drawings shown below:

## Slide 71
www.futuremanagers.com
Module 11: V-belt drives (continued)
CHECKING V-BELT SIZES AND LENGTHS
The first step is to measure the groove width to determine whether the belt is an ‘A’ or ‘B’ etc. section belt. The length is measured next, using a metal tape measure. Run the tape measure along the same route as the belt will run until you get back to where you started, then add on one belt thickness and you have the required length to within a few mm.

## Slide 72
www.futuremanagers.com
INTRODUCTION
A gear is a round disc with teeth at equal intervals around the outside edge (periphery). As with belt and chain drives, gears transmit rotary motion and power through the action of meshing teeth from one revolving shaft to another without slipping. A gear is like a wheel which engages (meshes) with other gears to transmit motion from one part of a mechanism to another.
Module 12: Gear drives

## Slide 73
www.futuremanagers.com
Module 12: Gear drives (continued)
TYPES OF GEARS
A shaft used with meshing gears can take one of three positions:
Gears and coupling shafts, run parallel to each other in the same plane.
Gears and coupling shafts where the centre lines intersect at an angle.
Gears, lying at angles to each other but not in the same plane.

## Slide 74
www.futuremanagers.com
Module 12: Gear drives (continued)
SAFETY PRECAUTIONS WHEN WORKING WITH, ON OR AROUND GEARS
Before you start work, ensure that environment is secured.
Follow all the required safety procedures regarding “lockout” and guarding/fencing before working on geared units.
Ensure that geared units are switched off and stationary before lubricating, changing speed, repairing, replacing the gear drive.
Make sure that gears are properly secured to the shaft.

## Slide 75
www.futuremanagers.com
Module 12: Gear drives (continued)
APPLICATIONS OF GEAR DRIVES
Gears are preferred over other types of drives in certain engineering settings. The following are reasons for this preference:
Where high levels of torque and power have to be transmitted.
Where the direction (same, opposite or different angle) of power transmission has to change.
Where there are restricted spaces.
Where varying rotating speeds (faster or slower) are needed

## Slide 76
www.futuremanagers.com
Module 12: Gear drives (continued)
THE DIFFERENCE BETWEEN A CYCLOID AND AN INVOLUTE GEAR TOOTH PROFILE
A cycloid is the curve generated by a point on the circumference of a moving circle when the circle rolls through a plane along a straight line.
The involute curve may be defined as the locus of a point on a piece of string that is pulled tight whilst being unwound from the circumference of the circle.

## Slide 77
www.futuremanagers.com
Module 12: Gear drives (continued)
THE PRINCIPLE OF VELOCITY RATIOS
Velocity ratio defines the rotational speed (rotational frequency) between a driver gear (input) and a driven gear (output) while they are engaged (meshed). Basically it is the number of times that the speed of the driver (input) gear is as great as that of the driven (output) gear. Velocity ratios are used in mechanical drawing and design to determine gear ratios, speed ratios, distance travelled by effort and loads etc.

## Slide 78
www.futuremanagers.com
Module 12: Gear drives (continued)
SIMPLE AND COMPOUND GEAR TRAINS
If a gear system consists of two gears, it is called a simple or singular gear train. If one gear turns clockwise, the other will automatically turn anti clockwise. These gears work in a straight line, and are fitted independently on their individual shafts.
A gear system consists of more than two gears (more than one pair of gears engaged), where the intermediate shaft has two gears fixed to it. It is called a compound gear train.

## Slide 79
www.futuremanagers.com
INTRODUCTION
Chain drives are used mainly to transmit mechanical power. A chain drive system is made up of a driving sprocket, one or more driven sprockets and an endless piece of chain that meshes with sprocket teeth.
Module 13: Chain drives

## Slide 80
www.futuremanagers.com
Module 13: Chain drives (continued)
SAFETY PRECAUTIONS WHEN WORKING WITH, ON OR AROUND CHAINS DRIVES
Protect people working on machines or in close range (proximity) especially in the case of chain breakage.
Protect machines against contaminants (dirt) and moisture from entering the chain drive system.
Protect the chain drive system in case of chain breakage.
Protect the chain drive system by supplying adequate lubrication.

## Slide 81
www.futuremanagers.com
Module 13: Chain drives (continued)
THE APPLICATIONS/USES OF CHAIN DRIVES
Chain drives are not as flexible as belt drives but are stronger and more efficient, because no slipping occurs.
Chain drives transmit power or motion from the driving to the driven sprocket.
Chain drives are used where a positive transmission is required.
Chain drives are used where tension in the drive is high (belts will slip).

## Slide 82
www.futuremanagers.com
Module 13: Chain drives (continued)
ADVANTAGES OF CHAIN DRIVES COMPARED TO GEARS AND BELT DRIVES
Transmission of power in chain drives is not achieved by friction.
Relatively high speeds can be maintained, the drive is compact. It can operate in both directions.
It is not affected by cold, heat or moisture.
Power transmission in chain drives can take place over a wide field.
Chain drives deliver a positive acceleration ratio.

## Slide 83
www.futuremanagers.com
Module 13: Chain drives (continued)
DISADVANTAGES OF CHAIN DRIVES COMPARED TO GEARS AND BELT DRIVES
The chain drive is absolutely direct and no slipping occurs.
Chain drives do no slip or creep (unlike belts), they maintain a positive speed ratio between the driving and driven sprockets.
Chain drives have an efficiency of 98% (no energy loss because of friction) and maintain a positive speed ratio over their entire life.
Chain drives are unaffected by heat or dust that ensures a long lifespan.

## Slide 84
www.futuremanagers.com
Module 13: Chain drives (continued)
CHAIN DRIVE TERMS
Sprockets for chain drives are precisely manufactured and the teeth are machined to standard specifications to obtain the correct contact between sprocket and chain.

## Slide 85
www.futuremanagers.com
Module 13: Chain drives (continued)
TYPES OF SPROCKETS
Types of sprockets include:
Driver sprocket;
Idler sprocket;
Driven sprocket; and
Sprocket pitch diameter.

## Slide 86
www.futuremanagers.com
Module 13: Chain drives (continued)
CHAIN LENGTH
Chain length can be determined accurately by taking the following factors into account:
Centre distance between sprockets (driver and driven);
Chain pitch;
Number of teeth on the (driver and driven); and
Arc of contact.

## Slide 87
www.futuremanagers.com
Module 13: Chain drives (continued)
CHAIN PITCH
The chain pitch is the distance in millimeters, between the centres of adjacent (next to) joint members. Chains can be classified in single pitch and double pitch roller chains. The pitch is the dimension which determines the other dimensions for a standard chain. A shorter pitch allows for higher operating speeds on a roller chain.

## Slide 88
www.futuremanagers.com
Module 13: Chain drives (continued)
TYPES OF CHAINS
Types of chains include:
Single and multiple-strand roller chains;
Double-pitch (extended-pitch) roller chains;
Silent (morse or inverted tooth) chains; and
Leaf chains.

## Slide 89
www.futuremanagers.com
Module 13: Chain drives (continued)
TYPES OF SPROCKETS
Types of sprockets include:
Solid sprockets;
Solid sprockets with spokes; and
Split sprockets with spokes.

## Slide 90
www.futuremanagers.com
Module 13: Chain drives (continued)
MAINTENANCE OF CHAIN DRIVES
To obtain a long and productive working life and keep down-time to a minimum, chain drives must be correctly maintained. Lubrication is necessary to minimise metal to metal contact of the pin-bushing joints in the chain. Oil should be applied to the outside and inside plate edges, as access to the pin-bushing areas is through the clearances between the plates.

## Slide 91
www.futuremanagers.com
Module 13: Chain drives (continued)
ALIGNING SPROCKETS AND TENSIONING CHAINS
Cautious and precise installation is of great importance for incident-free operation and long life. The following factors should be carefully observed:
Shift alignment;
Sprocket mounting;
Correct mounting of the chain; and
Chain tension.

## Slide 92
www.futuremanagers.com
SAFETY PRECAUTIONS TO BE OBSERVED WHEN WORKING WITH GEARS AND GEARBOXES
Always make sure that the power supply is disconnected before you touch a gear, it must be mechanically impossible for the gears to start turning while you are busy. Beware of sharp edges that have been formed by the teeth working against each other. The oil used in many gearboxes often has additives to which your skin could be allergic.
Module 14: Reduction gearboxes

## Slide 93
www.futuremanagers.com
Module 14: Reduction gearboxes (continued)
GENERAL USE OF GEARBOXES
Gearboxes are generally used for the purpose of altering gear ratios either to obtain more torque to overcome inertia or more speed with lower engine revolutions. When a small driver gear, drives a gear larger than itself, we get an increase in mechanical advantage.

## Slide 94
www.futuremanagers.com
Module 14: Reduction gearboxes (continued)
THE MAIN PARTS OF REDUCTION GEAR BOXES
A reduction gear-set
A worm-and-worm-wheel
A double reduction gear-set

## Slide 95
www.futuremanagers.com
INTRODUCTION
Pneumatics is the field of operation where compressed air is used to complete work.
Module 15: Pneumatics

## Slide 96
www.futuremanagers.com
Module 15: Pneumatics (continued)
THE BASIC COMPONENTS OF PNEUMATIC SYSTEMS
The compressor;
Air receivers;
Piping;
Valves; and
Actuating units.

## Slide 97
www.futuremanagers.com
Module 15: Pneumatics (continued)
DAILY MAINTENANCE OF PNEUMATIC SYSTEMS
Firstly, water traps and receivers must be drained daily to remove condensation build up. Receivers must be inspected and the inspection sheets signed on the dates stated. Piping and joints must be checked for leaks and corrosion. The oil level and oil filter changes on compressors must be monitored regularly. Output performance must be checked on an ongoing basis.

## Slide 98
www.futuremanagers.com
INTRODUCTION
Hydraulic systems are systems that can cause a force or movement by compressing fluid. They can be used as links between mechanical parts, thus eliminating the need for shafts, gears and connecting rods. Machine tools, motor vehicles, aircraft, jacks, missiles and ships are just a few applications of hydraulic systems.
Module 16: Hydraulics

## Slide 99
www.futuremanagers.com
Module 16: Hydraulics (continued)
UNITS OF MEASUREMENTS
Pressure measured in Pascals (Pa).
Flow rate measured in litres per second (/s).
Area measured in metres squared ().

## Slide 100
www.futuremanagers.com
Module 16: Hydraulics (continued)
FUNCTIONS OF HYDRAULIC FLUID
The main functions of hydraulic oil can be described as:
Oil transmits power readily because it is very slightly compressible.
The most desirable property of hydraulic oil is its lubricating ability.
Hydraulic oil must help resist corrosion of closely fitted components in the system.
This oil “take up” abrasive materials and contaminants or dirt and deposits them in the filter.

## Slide 101
www.futuremanagers.com
Module 16: Hydraulics (continued)
BASIC COMPONENTS/PARTS OF A HYDRAULIC SYSTEMS
Pumps;
Reservoir;
Pipes;
Valves;
Pressure relief valves; and
Non-return valves.

## Slide 102
www.futuremanagers.com
Module 16: Hydraulics (continued)
DIRECTIONAL CONTROL (SPOOL) VALVES
This type of valve is mainly used, as a result of its fast and positive reaction, to control the direction of flow of fluid. Directional control valves can be set in motion by electrical means (solenoid), by fluid (pilot) pressure or manually. Spool valves are versatile and can control fluid flow in a variety of parts of the hydraulic system. The contact area of spool valves has to be extremely accurately machined, lapped and fitted to prevent any leakages and to provide an efficient operation.

## Slide 103
www.futuremanagers.com
Module 16: Hydraulics (continued)
A SIMPLE HYDRAULIC CIRCUIT USING COMPONENTS

## Slide 104
www.futuremanagers.com
INTRODUCTION
A centre lathe is a machine tool that produces a cutting action by rotating the workpiece against the cutting edge of the cutting tool. The cutting tool can move diagonally across the bed or parallel to the lathe bed (sliding).
Module 17: Centre lathe

## Slide 105
www.futuremanagers.com
Module 17: Centre lathe (continued)
MANDRELS
Mandrels are sometimes called lathe arbors and are used to hold workpieces that are turned between centres. A mandrel is a hardened and tempered shaft used for holding workpieces that have already been bored and reamed to the correct size but need machining on other areas like gear cutting on the periphery.

## Slide 106
www.futuremanagers.com
Module 17: Centre lathe (continued)
DIFFERENT CLEARANCE ANGLES ON DIFFERENT LATHE CUTTING TOOLS
However superior a centre lathe may be, its efficient operation and the quality of the finished work will depend on the cutting tools used.
Whilst clearance angles differ slightly for different purposes, rake angles differs greatly depending on the metal being cut. The rake angle direction is mainly determined by the feed direction and the shape of the cutting edge.

## Slide 107
www.futuremanagers.com
Module 17: Centre lathe (continued)
FIXED AND TRAVELLING STEADIES FOR USE ON A CENTRE LATHE
Fixed and travelling steadies are used to give rigidity to long and thin workpieces. A steady prevents the workpiece from bending away from the cutting tool when it applies pressure during cutting.

## Slide 108
www.futuremanagers.com
Module 17: Centre lathe (continued)
DIFFERENT METHODS OF CUTTING TAPERS
Method 1: Use the setting over of the tailstock method and a clock gauge.
Method 2: Use the setting over of the tailstock method without a clock gauge.
Method 3: Use the compound slide.

## Slide 109
www.futuremanagers.com
Module 17: Centre lathe (continued)
BASIC INSTRUCTIONS FOR COMPUTERISED NUMERICAL CONTROLLED LATHE
The three basic instructional codes are:
G commands (G-codes): commands for specific cycles.
M commands (M-codes): for miscellaneous functions.
Positional data: movement on the x- and y-axis.

## Slide 110
www.futuremanagers.com
Module 17: Centre lathe (continued)
PROGRAMMING
Absolute programming: This makes use of absolute dimensions with all points of reference being taken from a common point.
Incremental programming: This is done by taking the distance from one point to the next on the workpiece, not from a common point.

## Slide 111
www.futuremanagers.com
Module 17: Centre lathe (continued)
THE BASIC PRINCIPLES OF PROGRAMMING A COMPUTER CONTROLLED LATHE
The location of each operation in co-ordinate format.
The sequence of operations and the selection of tools.
Cutting speeds and feed rates and the length and depth of cuts.
When and where to apply cutting fluid, how much and for how long.

## Slide 112
www.futuremanagers.com
INTRODUCTION
Surface grinding is fundamentally a finishing process, designed to provide close dimensional accuracy with improved surface finish, usually on work that has been machined previously. Material is removed (cut-away) by means of a grinding wheel which may be considered a multi-toothed cutter. These cutting teeth or edges are formed by a large number of abrasive particles which are securely held together throughout the grinding wheel by means of a suitable bond.
Module 18: Surface grinding machines

## Slide 113
www.futuremanagers.com
Module 18: Surface grinding machines (continued)
FUNCTION
Surface grinding is the precision grinding of a planed surface. While all grinding, strictly speaking, is surface grinding, the term is commonly used to describe the grinding of flat surfaces. Many parts previously milled, planed or hand scraped, are now precision ground. With the introduction of large, high-powered surface grinders, it is obvious that steel or other metals are actually machined away.

## Slide 114
www.futuremanagers.com
Module 18: Surface grinding machines (continued)
GRINDING WHEELS
Grinding wheels are not natural stones, but grains of abrasive material bonded together at high temperature. The abrasive material is either aluminium oxide, which is ideal for grinding steel tools, or silicon carbide, which is good for brass, aluminium or copper.

## Slide 115
www.futuremanagers.com
Module 18: Surface grinding machines (continued)
GRINDING WHEEL PROFILES
Disc grinding (straight) wheel;
Cup grinding wheel;
Flaring cup grinding wheel.

## Slide 116
www.futuremanagers.com
Module 18: Surface grinding machines (continued)
GLASING OF GRINDING WHEEL
The condition of a grinding wheel is easily recognised by the shiny appearance on the grinding face of the grinding wheel. Glasing occurs when the abrasive grains become dulled or blunt and do not break away from the bond to reveal fresh grain.

## Slide 117
www.futuremanagers.com
Module 18: Surface grinding machines (continued)
TYPES OF MAGNETIC CHUCKS
Common magnetic chuck used on reciprocating surface grinder.
A permanent magnetic chuck often used where wiring would be inconvenient.
Vacuum chucks used for practically anything and considered good for thin workpieces.
Magnetic sine chuck used for grinding workpieces with non-parallel surfaces.

## Slide 118
www.futuremanagers.com
INTRODUCTION
A milling machine provides the cutting action to a rotating cutting tool. In milling, a multi –toothed cutter rotating in a fixed position on the machine, shapes the workpiece as it is traversed across the cutter. The workpiece is firmly and safely secured in a machine vice or on the machine table, which can be adjusted to set the depth of cut and can be traversed in at least two directions on the horizontal plane.
Module 19: Milling machines

## Slide 119
www.futuremanagers.com
Module 19: Milling machines (continued)
DIVIDING HEAD
A dividing head is a supplementary accessory on a milling machine. The dividing head breaks up the circumference of a circular workpiece into a number of equal divisions. A dividing head is mounted on the milling machine table and used to work between centres in conjunction with the tailstock, or it can be fitted with a chuck for the direct mounting of work.

## Slide 120
www.futuremanagers.com
Module 19: Milling machines (continued)
INDEX PLATE
The aim of the index plate with its confusion of holes is to enable one revolution of the crank to be further subdivided into fractions of a revolution, especially where the fraction is not a factor of 40. The index plate is provided with a number of circles each with a different number of holes. Hole circles in the index plate provide the indexing function.

## Slide 121
www.futuremanagers.com
Module 19: Milling machines (continued)
INDEXING ON A DIVIDING HEAD
There are basically five methods of indexing:
Simple indexing;
Rapid indexing;
Angular indexing;
Differential indexing; and
Graduating (cutting accurate graduations or rack pitches).

## Slide 122
www.futuremanagers.com
Module 19: Milling machines (continued)
MILLING CUTTERS
A great variety of cutters is available and of these, a number are made for direct mounting in the spindle nose, for mounting on stub arbors or for holding in special chucks. The general types of milling cutters may be classified as:
Arbor cutters; plain, side and face, staggered-tooth and metal slitting saw.
Shank cutters: end mills, T-slot and Woodruff key cutter.

## Slide 123
www.futuremanagers.com
Module 19: Milling machines (continued)
ANGLES OF MILLING CUTTERS

## Slide 124
www.futuremanagers.com
Module 19: Milling machines (continued)
LAND
The land is the surface on the periphery of a rotary cutting tool, such as a milling cutter, drill, tap or reamer, which joins the face of the flute or tooth to make up the basic cutting edge. The land is relieved to prevent interference between itself and the surface being machined (workpiece). A raised land allows for several sharpening before a secondary clearance has to be grounded.

## Slide 125
www.futuremanagers.com
Module 19: Milling machines (continued)
METHODS OF MILLING
Different methods of milling include:
Up (conventional) milling;
Plain or slab milling;
Straddle milling; and
Gang milling.